## Slide 1
Physical Design of
RISC-V based
System-on-Chip
using OpenLane
25VL742 — Physical Design
24 March 2026
Group AG-10
Ajith Sai Visal
CB.EN.P2VLD25002
Arvind Narayan B
CB.EN.P2VLD25004
Department of Electronics and Communication Engineering
Amrita School of Engineering
Amrita Vishwa Vidyapeetham, Coimbatore – 641112
1

## Slide 2
Aim
25VL742 Physical Design | Group AG-10 | Amrita Vishwa Vidyapeetham
To implement the complete physical design of a RISC-V based PicoSoC using the open-source OpenLane EDA flow targeting the SkyWater SKY130 130 nm PDK, and complete the RTL to GDS II flow
SCOPE OF WORK
01
Design
RISC-V PicoSoC (RV32IMC)
PicoRV32 + UART + SPI
SRAM + Memory Decoder
SKY130 130 nm PDK
02
Flow
RTL Simulation
Synthesis → Floorplan
CTS → Routing
DRC + LVS + STA
03
Goals
Timing closure @ 100 MHz
Zero DRC violations
LVS clean sign-off
Tapeout-quality GDS
2

## Slide 3
Abstract
25VL742 Physical Design | Group AG-10 | Amrita Vishwa Vidyapeetham
Project
Complete physical design of a RISC-V based PicoSoC using open-source OpenLane targeting SkyWater SKY130 130 nm PDK
Architecture
PicoRV32 CPU (RV32IMC) + UART + SPI Flash Controller + SRAM — all on a 32-bit system bus
Flow
RTL simulation (Icarus Verilog) → Synthesis (Yosys) → Floorplan → CTS → Routing → DRC + LVS sign-off
Runtime
OpenLane completed in 1h 21m | 42,194 synthesized cells | Die area: 2.41 mm²
Timing
Timing closure at 100 MHz — WNS = 0.0 ns, TNS = 0.0 ns | DRC: 0 violations | LVS: Clean
Routing
~2.99 million µm wire length | 368,965 vias | 6 metal layers (li1, met1–met5)
Conclusion
Confirms open-source VLSI tools are capable of tapeout-quality physical design in academic settings
3

## Slide 4
PicoSoC Architecture
25VL742 Physical Design | Group AG-10 | Amrita Vishwa Vidyapeetham
PicoSoC Overall Block Diagram
Fig. 1: PicoSoC Block Diagram
PicoRV32 Simplified Block Architecture
Fig. 2: PicoRV32 Simplified Block Architecture [1]
4

## Slide 5
Module Block Diagrams
25VL742 Physical Design | Group AG-10 | Amrita Vishwa Vidyapeetham
UART
Fig. 3: UART Block Diagram
SPI Flash Controller
Fig. 4: SPI Block Diagram
Memory
Fig. 5: Memory Block Diagram
PICOSOC MEMORY MAP
Fig. 5: Memory Block Diagram
5

## Slide 6
RTL to GDS II Flow
25VL742 Physical Design | Group AG-10 | Amrita Vishwa Vidyapeetham
Fig. 6: RTL to GDS II Physical Design Flow using OpenLane (SKY130 PDK)
6

## Slide 7
Methodology
25VL742 Physical Design | Group AG-10 | Amrita Vishwa Vidyapeetham
Front End Flow
RTL Design
Verilog HDL — PicoRV32, UART, SPI, SRAM, Memory Decoder
RTL Simulation
Icarus Verilog — functional verify, golden waveform
Synthesis
Yosys + ABC → sky130_fd_sc_hd | AREA 0 strategy
Pre-Layout STA
OpenSTA — setup/hold timing verified at 100 MHz
Back End Flow
Floorplanning & PDN
OpenROAD — macro placement, power straps, die 1547×1558 µm
Placement
RePlAce (global) + OpenDP (detailed) | antenna diodes
CTS
TritonCTS — balanced clock tree | skew: 0.29 ns
Routing & Sign-off
FastRoute + TritonRoute | Magic DRC | Netgen LVS | OpenSTA
7

## Slide 9
Results: Floorplanning & Placement
25VL742 Physical Design | Group AG-10 | Amrita Vishwa Vidyapeetham
4.1 Floorplanning & PDN — OpenROAD
Fig. 8: Complete Detailed routing – Open Road Visualization
4.2 Placement & Routing — RePlAce + OpenDP
Fig. 7: Standard cell placement — (KLayout)
9

## Slide 10
Area Comparison — Macro Die Areas
25VL742 Physical Design | Group AG-10 | Amrita Vishwa Vidyapeetham
Macro-level die areas and placement coordinates — Base Paper [1] vs this implementation.
Table 1: Macro-level Die Area & Placement Coordinates — Base Paper [1] vs This Work
OVERALL CHIP AREA METRICS
Table 2: Overall Chip Area Metrics — Base Paper [1] vs This Work
10

## Slide 11
Comparison — Performance Metrics
25VL742 Physical Design | Group AG-10 | Amrita Vishwa Vidyapeetham
Key performance metrics compared. Maximum operating frequency is the primary improvement over the base paper [1].
Table 3: Performance Metrics Comparison — Base Paper [1] vs This Work
Key Observation
This implementation achieves 100 MHz — 5× higher than the base paper's 19 MHz — by applying a 10 ns clock period constraint (10× tighter). All physical verification metrics (die area, DRC, LVS) are identical or better.
11

## Slide 12
Results: Clock Tree Synthesis — Timing
25VL742 Physical Design | Group AG-10 | Amrita Vishwa Vidyapeetham
Post-CTS timing results. Base paper used 100 ns constraint; this work uses 10 ns (100 MHz).
Table 4: CTS Timing Results — This Work vs Base Paper
Key Observation
This implementation targets 10 ns (100 MHz) — 10× tighter than the base paper's 100 ns constraint. TritonCTS achieved a clock skew of 0.29 ns, demonstrating excellent clock distribution for a 42,194-cell multi-macro SoC design.
12

## Slide 13
Results: Global Routing — Layer Utilization
25VL742 Physical Design | Group AG-10 | Amrita Vishwa Vidyapeetham
Routing resource utilization per metal layer after FastRoute. Base paper does not report per-layer utilization.
Table 5: Metal Layer Routing Utilization — FastRoute (This Work)
Key Observation
met1 (33.24%) and met2 (34.32%) carry the highest routing load — consistent with SKY130 standard cell routing. li1 (0%) is reserved for standard cell internal connections. Total: 2,986,170 µm wire length and 368,965 vias.
13

## Slide 14
Results: DRC + LVS Physical Sign-off
25VL742 Physical Design | Group AG-10 | Amrita Vishwa Vidyapeetham
Physical verification results compared with the base paper [1].
Table 6: Physical Sign-off Results — This Work vs Base Paper
Key Observation
Both this work and the base paper achieved DRC-clean and LVS-clean results. Antenna violations (432 pin, 326 net) were fully resolved via antenna diode insertion — a standard physical design practice for designs of this scale.
14

## Slide 15
Results: Post-Layout STA — Timing
25VL742 Physical Design | Group AG-10 | Amrita Vishwa Vidyapeetham
Final timing sign-off on the fully routed netlist (OpenSTA). 100 MHz is 5× better than base paper.
Table 7: Post-Layout STA Results — This Work vs Base Paper [1]
Key Observation
Maximum operating frequency of 100 MHz is 5× higher than the base paper's 19 MHz. Both designs achieve WNS = TNS = 0.0 ns, confirming full timing closure under their respective constraints.
15

## Slide 16
Results: Post-Layout STA — Power & Summary
25VL742 Physical Design | Group AG-10 | Amrita Vishwa Vidyapeetham
Power consumption and design summary metrics from the final routed implementation.
Table 8: Power & Summary Metrics — This Work vs Base Paper [1]
16

## Slide 18
Results: GDS II Output
25VL742 Physical Design | Group AG-10 | Amrita Vishwa Vidyapeetham
Full Chip Layout — KLayout 0.28.16
Fig. 9: Complete PicoSoC GDS II layout (Metal Layers hidden) — KLayout
Zoomed-in Layout View
Fig. 10: Zoomed view — standard cells, routing & vias
▸
Streamed using Magic after DRC, LVS & antenna sign-off
▸
All 5 macros within 1546.9 × 1557.6 µm die boundary
▸
Outputs: picosoc.gds · picosoc.lef · picosoc.spef
18

## Slide 19
Inference
25VL742 Physical Design | Group AG-10 | Amrita Vishwa Vidyapeetham
Flow Completion
OpenLane RTL-to-GDS completed in 1h 21m — confirming open-source EDA viability for complete SoC physical design
Timing Closure
100 MHz achieved (WNS = TNS = 0.0 ns) — 5× better than base paper's 19 MHz
Physical Verification
Magic DRC: 0 violations | Netgen LVS: clean | 53,216 nets matched
CTS Quality
TritonCTS achieved 0.29 ns clock skew — excellent for a 42,194-cell multi-macro SoC
Routing
met1 (33.24%) and met2 (34.32%) carry highest utilization — consistent with SKY130
Antenna
432 pin and 326 net violations resolved via diode insertion — standard for this scale
Power
155 mW at typical corner — majority in combinational logic, expected for processor-centric design
Area & Placement
20.43% density vs 20% target — correct placer operation, sufficient routing headroom
19

## Slide 20
Reference
25VL742 Physical Design | Group AG-10 | Amrita Vishwa Vidyapeetham
[1]
M. Fauzan, R. F. Yanuarsyah, M. H. Hibatullah, R. Arisaputra, I. Syafalni, N. Sutisna, T. Adiono, and M. Ikeda,
"Physical Design of RISC-V based System-on-Chip using OpenLane,"
2024 IEEE Asia Pacific Conference on Circuits and Systems (APCCAS), pp. 529–533, Nov. 2024.
DOI: 10.1109/APCCAS62602.2024.10808656
20

## Slide 21
Thank You
Physical Design of RISC-V based System-on-Chip using OpenLane
Group AG-10 | 25VL742 Physical Design | Amrita Vishwa Vidyapeetham
21